## Slide 1: Topology of NTP Server for Redundancy
10.1.1.2 NTP SERVER
Office/Fab PC/NT
UNIX Servers
Office/Fab PC/NT
UNIX Servers
Synchronization frequency:
NT-- 60 minutes
PC– 8 Hours
10.1.1.3 NTP SERVER
Network TCP/IP
Master
slave
The NTP server IP of all the clients should be set as10.1.1.1
10.1.1.2
10.1.1.1
10.1.1.3
10.1.1.1is the virtual IP of the port eth2; 10.1.1.1 and 10.1.1.2 or 10.1.1.3 are from the same port
GPS antenna
GPS Time Server
Notes: <number>

## Slide 2: Status 1: Master and slave servers are both working normally
10.1.1.2 NTPSERVER
Office/Fab PC/NT
UNIX Servers
Office/Fab PC/NT
UNIX Servers
Synchronization Frequency:
NT-- 60 minutes
PC– 8 hours
10.1.1.3 NTPSERVER
Network TCP/IP
Master
slave
The NTP server IP of all the clients should be set as10.1.1.1
10.1.1.2
10.1.1.1
10.1.1.3
The IP will not float when both the master and slave server are working well or have problems at the same time
Notes: <number>

## Slide 3: Status 2: Master server performs normally, but slave server has problem
10.1.1.2 NTPSERVER
Office/Fab PC/NT
UNIX Servers
Office/Fab PC/NT
UNIX Servers
Synchronization frequency:
NT-- 60 minutes
PC– 8 hours
10.1.1.3 NTPSERVER
NetworkTCP/IP
Master
slave
The NTP server IP of all the clients should be set as10.1.1.1
10.1.1.2
10.1.1.1
10.1.1.3
When master can get satellite signal but slave can not or when the root error of the master is abnormal but of the slave is normal, 10.1.1.1 will float to the other server.
Notes: <number>

## Slide 4: Status 3: When there are network problems between master and slave server
10.1.1.2 NTPSERVER
Office/Fab PC/NT
UNIX Servers
Office/Fab PC/NT
UNIX Servers
Synchronization frequency:
NT-- 60 minutes
PC– 8 hours
10.1.1.3 NTPSERVER
Network TCP/IP
Master
slave
The NTP server IP of all the clients should be set as10.1.1.1
10.1.1.2
10.1.1.1
10.1.1.3
10.1.1.1
When there are network problems, both the master and slave will use the virtual IP 10.1.1.1. As soon as the network problems are solved, the IP 10.1.1.1 will float to the server whose status is better than the other’s, and the other server will not use the virtual IP.
Notes: <number>

## Slide 5: Status 4: When the master and slave can communicate normally
10.1.1.2 NTPSERVER
Office/Fab PC/NT
UNIX Servers
Office/Fab PC/NT
UNIX Servers
Synchronization Frequency:
NT-- 60 minutes
PC– 8 hours
10.1.1.3 NTPSERVER
NetworkTCP/IP
Master
slave
The NTP server IP of all the clients should be set as10.1.1.1
10.1.1.2
10.1.1.1
10.1.1.3
Notes: <number>